Dokumentation
metraTec LPC 122x Bootloader

Datum: July 2012

Version: 0.2 (not complete, work in progress)
# Inhalt

# Data formats
## met-File format
Addr.	Len	Name	Format	Example
0	16	Hardware Name	ASCII	“DwarfZ XR “
16	16	Firmware Name	ASCII	“Receiver Stick “
32	4	Hardware Rev.	ASCII	“0100“
36	4	Firmware Rev.	ASCII	“0101“
40	2	Number of Code-Blocks (n)	uint16 (MSB first)	0x01, 0x3A (0x013A)
42	n*259	n Code-Blocks	send blocks consecutively

The met-File also contains a CRC. The respective place is kept free in the firmware bin file! So its part of the Code Blocks.
## Code-Block format
Addr.	Len	Name	Format
0	1	Write Command	uint8 0x02 (write)
1	2	Block Number	uint16 ( MSB first)
3	256	Encrypted Code	256*uint8

## Command format:
Addr.	Len	Name	Format	Example
0	2	Length of data (not including CRC and Length itself)	uint16 ( MSB first)	0x01, 0x03 (259)
2	1	Command	uint8	0x0A (Flash erase)
3	n	Parameter	command dependent
n+3	2	CRC-16 over command and parameter	uint16 (MSB first)

Length of parameter (n) is determined by command.
## Response format
Addr.	Len	Name	Format	Example
0	2	Length of data (not including CRC and Length itself)	uint16 ( MSB first)	0x00, 0x02 (2)
2	1	Command	uint8 (Request-Cmd + 0x80)	0x8A
3	1	Error Code	uint8	0x00
4	n	Parameter	command dependent
n+4	2	CRC-16 over command and parameter	uint16 (LSB first)

Length of parameter (n) is determined by command.
# Commands

Handshake (0x01):	To check if there is a reader. No function
Parameter:	none
Answer:	Empty
Write_Code (0x02):	Code-Block transfer
Parameter:	see Code-Block format
Answer:	Empty
Read_SN (0x03):	Read serial number
Parameter:	none
Answer:	16 Byte Serial Number
Read_HW_Name (0x04):	Read Hardware Name
Parameter:	none
Answer:	16 Byte Hardware Name
Read_HW_Rev (0x05):	Read Hardware Revision
Parameter:	none
Answer:	4 Byte Hardware Revision
Read_FW_Name (0x06):	Read Firmware Name
Parameter:	none
Answer:	16 Byte Firmware Name
Read_FW_Rev (0x07):	Read Flash Size
Parameter:	none
Answer:	4 Byte Firmware Revision
Read_Flash_Size(0x08):	Read Flash Size in Byte
Parameter:	none
Answer:	4 Byte uint32 MSB first

Erase_Flash (0x0A):	Erase Flash before writing Code
Parameter:	none
Answer:	Empty
Read_BTL_Rev (0x0C):	Read Bootloader Revision
Parameter:	none
Answer:	4 Byte Bootloader Revision
Read_BTL_Name (0x0D):	Read Bootloader Name
Parameter:	none
Answer:	16 Byte Bootloader Name
Set_Timeout (0x10):	Set Command Receive Timoutvalue in milliseconds.
Startup value is 50ms.
Parameter:	uint16 MSB first
Answer:	none
Reset (0x41):	Hardware Reset
Parameter:	none
Answer:	Empty
Write_SN (0x43):	Write serial number
Parameter:	serial number (16 ASCII)
Answer:	Empty
Write_HW_Name (0x44):Write Hardware Name
Parameter:	hardware name (16 ASCII)
Answer:	Empty
Write_HW_Rev (0x45):	Write Hardware Revision
Parameter:	hardware revision (4 ASCII)
Answer:	Empty

## Error Codes

Code	Error
0x00	Success
0x01	Failure
0x02	Invalid Command
0x03	CRC error
0x04	Invalid Block Number
0x07	Flash not erased
0x0A	UART Timeout
0x3D	Watchdog occurred
0xB0	Brownout occured

# Communication Sequences

## How to get in touch with the bootloader

Establish an UART connection with 115200 Baud 8N1 to the device. If there is no firmware the bootloader will start. If there is a firmware use the command BTL to start the bootloader (or whatever your firmware uses as command).

## How to get in touch with the bootloader (advanced)

If there is firmware without working BTL command you can contact the bootloader by sending an ASCII ‘i’ (0x69) within 5 to 55 ms after power up or firmware reset (“RST<CR>”) if compiled with the respective part in main.c
If the bootloader is started by this method it will return ASCII ‘L’ (0x4C). After this you can proceed with the firmware update.
## First Startup Procedure

Setting the following parameters is only possible once after flashing the bootloader.
Write serial number	0x83 SN(16 ASCII) <CRC16>
Response:	0xC3 0x00 <CRC16>	(Success)
0xC3 0x01 <CRC16>	(Already written)
0xC3 0x03 <CRC16>	(CRC error)
Write Hardware Name	0x84 HW_Name(16 ASCII) <CRC16>
Response:	0xC4 ... (see Write_SN)
Write Hardware Revision	0x85 HW_Rev(4 ASCII) <CRC16>
Response:	0xC5 ... (see Write_SN)

## Firmware Update Procedure

Read Hardware Name	0x04 0xA3 0x49
Response:	0x84 0x00 HW_Name(16 ASCII) <CRC16>
Compare read HW_Name to Hardware Name in met-File

Read Hardware Revision	0x05 0x2A 0x58
Response:	0x85 0x00 HW_Rev(4 ASCII) <CRC16>
Compare first two chars of the read HW_Rev to Hardware Revision in met-File

Erase Flash	0x0A 0xDD 0xA0
Response:	0x8A 0x00 <CRC16>	(Success)
0x8A 0x03 <CRC16>	(CRC error)

Read Number of Blocks (n) from met-File (Addr: 41-42, uint16 (LSB first))

Repeat for (i=0; i<n; i++):
Write Code	met-File[261*i + 43], length = 261
Response:	0x82 0x00 <CRC16>	(Success)
0x82 0x03 <CRC16>	(CRC error)
0x82 0x04 <CRC16>	(Invalid Block Number)
0x82 0x06 <CRC16>	(HW match error)
0x82 0x07 <CRC16>	(Flash not erased)
0x82 0x08 <CRC16>	(Flash too small)

Reset	0x41 0x0A 0x5C
Response:	0xC1 0x00 <CRC16>	(Success)
0xC1 0x03 <CRC16>	(CRC error)
# Versionsübersicht
Version	Änderung	Bearbeitet durch	Datum
0.1	Erstellt	MK	19.07.2012

Contact / Support
metraTec GmbH
Werner-Heisenberg-Str. 1
D-39106 Magdeburg

Tel.: +49 (0)391 251906-00
Fax: +49 (0)391 251906-01

Email:	support@metratec.com
Web:	http://www.metratec.com

Copyright

© Copyright 2012
All rights reserved by metraTec GmbH, Magdeburg, Germany.

The content of this document is subject to change without prior notice. Copying is permitted for internal use only or with written permission by metraTec. metraTec is a registered trademark of metraTec GmbH. All other trademarks are the property of their respective owners.